## Slide 1: Soldering Workshop
Led by Ethan Tabler

## Slide 2: What is solder and why do we use it?

## Slide 3: Solder is...
Metal
  Several types of metal, typically alloyed
  Lead vs lead-free
Flux
  Rosin flux helps the mechanical strength and electrical contact of electrical joints
More permanent
  Breadboards are for quick testing
  Soldered circuits are sturdy and more reliable
Notes: Why do we use solder?

## Slide 4: Solder can be used to...
Electrically connect components
  Conductive
  Can be used in place of wiring
Mechanically connect components
  Strength varies with alloy/mix
  Take a look at your potentiometers!
What about non-electrical uses?

## Slide 5: What other tools might be helpful?
Solder wick
Tweezers
Solder sucker
Wire cutters
Wet sponge
Silicone Pad
Tip cleaner (brass)
Wire stripper
Microscope
Helping Hand
Notes: Solder wick, Tweezers, Solder sucker, Wire cutters, Wet sponge, Silicone Pad, Tip cleaner (brass), Wire stripper, Microscope, Helping Hand

## Slide 6: Soldering Iron Tips
Different tips are used for specific purposes
  Finer tips are used for SMD parts and smaller TH devices
  Thicker, wedge-shaped tips are used for larger components or mechanical joints
Larger tips have more thermal mass and can melt solder faster

## Slide 7
Surface-Mount
Through-Hole
Only mounted on one side of the board; harder to solder
Part physically goes through the board; easier to solder

## Slide 8: Demonstration
Notes: Perfboard with 2 resistors per person, solder bridging → (smaller components first) through-hole on PCB, SMD cap → Will/jackie does speaker/battery; Ethan does hot air solder for SOIC → finish with potentiometer
Option of solder sucker/solder wick at the end